Bryan Turek

-

Experiment #7 – 8-Bit Patterns and Keyboard Input
CPE 311 S-001

Lab Partner: Tyler Durham

-

09/12/2013
Introduction:

The goal of this lab is to utilize the I8086's logical and bit manipulation instructions to generate various bit patterns. These patterns will be displayed across an 8-bit LED interface that was designed in a previous lab.

Exercise 1:

Experiment:	This experiment involves creating 3 distinct bit patterns. The patterns will start with an
initial value loaded into a register at step 1.

Results:	Using only logical operators we transitioned from the initial step to the next steps:

Pattern One:

Assume cs:code, ds:data, ss:stack

data segment
; All variables defined within the data segment
message db "Lab 5 Exercise 1$"
var db "w"
storage db 17 DUP(" ")
data ends

stack segment
;Stack size and the top of the stack defined in the stack segment
dw 100 dup(?)
stacktop:
stack ends

code segment
begin:
mov ax, data
mov ds,ax
mov ax, stack
mov ss,ax
mov bx,0
mov sp, offset stacktop

MOV DX,143H
MOV AL, 02H
OUT DX,AL

;This sets the control register to direction mode

MOV DX, 141H
MOV AL, 0FFH
OUT DX, AL

;this tells the control register
;that all of the pins in port b are outputs

MOV DX, 143H
MOV AL, 03H
OUT DX, AL

;this sets the control register to operation mode

MOV DX, 141H

MOV AL, 01000010b

asdf:
MOV CX, 07H
abc:
OUT DX, Al
NOT AL
call delay
MOV CX, 07H
JMP asdf
;this is a infinite loop that turns on and off all of the LEDs

delay:
;push and pop commands should be here but are not necessary
push cx
push bx
mov cx, 0fH
outerloop:
mov bx, 0ffffh
innerloop:
nop
dec bx
jnz innerloop
dec cx
jnz outerloop
pop bx
pop cx
ret
;this is the delay operation that gives the LEDs enough time to turn on and off, altogether this command runs 4096 times
code ends
end begin

Pattern Two:

Assume cs:code, ds:data, ss:stack

data segment
; All variables defined within the data segment
message db "Lab 5 Exercise 1$"
var db "w"
storage db 17 DUP(" ")
data ends

stack segment
;Stack size and the top of the stack defined in the stack segment
dw 100 dup(?)
stacktop:
stack ends

code segment
begin:
mov ax, data
mov ds,ax
mov ax, stack
mov ss,ax
mov bx,0
mov sp, offset stacktop

MOV DX,143H
MOV AL, 02H
OUT DX,AL

;This sets the control register to direction mode

MOV DX, 141H
MOV AL, 0FFH
OUT DX, AL

;this tells the control register
;that all of the pins in port b are outputs

MOV DX, 143H
MOV AL, 03H
OUT DX, AL

;this sets the control register to operation mode

MOV DX, 141H

MOV AL, 01111111b

asdf:
MOV CX, 07H
abc:
OUT DX, Al
ROR AL, 1
call delay
loop abc
MOV CX, 07H
def:
OUT DX, Al
ROL AL, 1
call delay
loop def
JMP asdf
;this is a infinite loop that turns on and off all of the LEDs

delay:
;push and pop commands should be here but are not necessary
push cx
push bx
mov cx, 0fH
outerloop:
mov bx, 0ffffh
innerloop:
nop
dec bx
jnz innerloop
dec cx
jnz outerloop
pop bx
pop cx
ret
;this is the delay operation that gives the LEDs enough time to turn on and off, altogether this command runs 4096 times
code ends
end begin

Pattern Three:

Assume cs:code, ds:data, ss:stack

data segment
; All variables defined within the data segment
message db "Lab 5 Exercise 1$"
var db "w"
storage db 17 DUP(" ")
data ends

stack segment
;Stack size and the top of the stack defined in the stack segment
dw 100 dup(?)
stacktop:
stack ends

code segment
begin:
mov ax, data
mov ds,ax
mov ax, stack
mov ss,ax
mov bx,0
mov sp, offset stacktop

MOV DX,143H
MOV AL, 02H
OUT DX,AL

;This sets the control register to direction mode

MOV DX, 141H
MOV AL, 0FFH
OUT DX, AL

;this tells the control register
;that all of the pins in port b are outputs

MOV DX, 143H
MOV AL, 03H
OUT DX, AL

;this sets the control register to operation mode

MOV DX, 141H

MOV AL, 11111111b
MOV CX, 1111000011111111b
MOV BX, 1111111100001111b

asdf:
MOV al, cl
and al, bh
OUT DX, Al
call delay
abc:
ROR CX,1
ROL BX,1
MOV al, cl
and al, bh
OUT DX, Al
call delay
cmp al, 11000011b
jne abc
def:
ROL CX,1
ROR BX,1
MOV al, cl
and al, bh
OUT DX, Al
call delay
cmp al, 11111111b
jne def
JMP asdf
;this is a infinite loop that turns on and off all of the LEDs

delay:
;push and pop commands should be here but are not necessary
push cx
push bx
mov cx, 0fH
outerloop:
mov bx, 0ffffh
innerloop:
nop
dec bx
jnz innerloop
dec cx
jnz outerloop
pop bx
pop cx
ret
;this is the delay operation that gives the LEDs enough time to turn on and off, altogether this command runs 4096 times
code ends
end begin

Exercise 2:

Experiment:	The goal of this exercise is to allow the keyboard to be used as an input device in an	assembly program.

Results:	Using two functions of interrupt 21H can be used to allow for input from the keyboard.	01H function will halt normal program execution until a key is pressed from the	keyboard. 08H function will do the same thing excepts 01H echoes the input back to the	screen, 08H will not do this. The code is below:

Assume cs:code, ds:data, ss:stack

data segment
; All variables defined within the data segment
message db "Please enter a string:$"
keyboard db 20 dup(?)
data ends

stack segment
;Stack size and the top of the stack defined in the stack segment
dw 100 dup(?)
stacktop:
stack ends

code segment
begin:
mov ax, data
mov ds,ax
mov ax, stack
mov ss,ax
mov sp, offset stacktop

Mov ah, 2

Mov si, offset message

Abc:
Mov dl,[si]
Cmp dl,"$"
Je keys
Int 21h
Inc si
Jmp abc
;the above abc loop simply copies the contents of memory
;byte by byte, at the address that si points to.
;It prints these bytes until it it reaches the dollar sign and exits
keys:
mov si, offset keyboard
mov ah, 01H
mov cx, 14H
def:
int 21h
cmp AL, 0DH
je print
mov [si], al
inc si
loop def

print:
mov al, "$"
mov [si], al
Mov si, offset keyboard
mov ah, 2
mov dl, 0Dh
int 21h
mov dl, 0Ah
int 21h
ghi:
Mov dl,[si]
Cmp dl,"$"
Je End_prog
Int 21h
Inc si
Jmp ghi

End_prog:
Mov ah, 4ch
Int 21h
;end code

;THIS IS WHERE YOUR CODE ENDS
code ends
end begin

Conclusion:

By utilizing the I8086's logical and bit manipulation instructions we were able to develop bit patterns to be used with and 8-bit LED interface. Also using what we have learned up till this point allowed us to use Keyboard Interrupts to print a string entered by the user to the screen. In conclusion this lab helped us understand more about the I/O ports for computers.