Bryan Turek

-

Experiment #6 – Digital Output for the I8086
CPE 311 S-001

Lab Partner: Tyler Durham

-

09/12/2013
Introduction:

The goal of this lab is for students to learn how to perform digital output using the Octagon 6040's input/output ports. The Octagon 6040 contains 24 programmable I/O lines that can be individually programmed to serve as a digital input or output.

Exercise 1:

Experiment:	The goal of this experiment is to design and build a circuit that connects all 8 outputs of	Port B to separate LEDs.

Results:

Vdd = 5V
Vled= 1.7
Do KVL ->Voltage on the resistor = 3.3V
Use ohm’s law R= {V} over {I} = {3.3} over {10* {10} ^ {-3}} = 330 Ω

Exercise 2:

Experiment:	The goal of this experiment is to create a program to configure all 8 lines as outputs and	create an endless loop that continuously turns the LEDs on Port B on and off.

Results:	Using previous experiment results we created a program to configure all 8 lines as	outputs and create an endless loop that continuously turns the LEDs on and off.
The results of the code are as follows:

Assume cs:code, ds:data, ss:stack

data segment
; All variables defined within the data segment
message db "Lab 5 Exercise 1$"
var db "w"
data ends

stack segment
;Stack size and the top of the stack defined in the stack segment
dw 100 dup(?)
stacktop:
stack ends

code segment
begin:

mov dx, 143h
mov al, 02h
out dx, al

mov dx, 141h
mov al, 0ffh
out dx, al

mov dx, 143h
mov al, 03h
out dx, al

mov ax, data
mov ds,ax
mov ax, stack
mov ss,ax
mov sp, offset stacktop

Abc:
mov dx,131h
mov al, 0
out dx, al
mov al, 0ffh
out dx, al
jmp abc

code ends
end begin

Exercise 3:

Experiment:	The objective of this exercise is to provide the LEDs with a time delay that gives enough	time to make the transition between one state to the other. To create a delay, clock cycles	must be wasted by the processor having no impact on the output.

Results:	Adding to the previous experiment we created a time delay which waits before firing	using NOP. Code below:

Assume cs:code, ds:data, ss:stack

data segment
; All variables defined within the data segment
message db "Lab 5 Exercise 1$"
var db "w"
data ends

stack segment
;Stack size and the top of the stack defined in the stack segment
dw 100 dup(?)
stacktop:
stack ends

code segment
begin:

mov ax, data
mov ds,ax
mov ax, stack
mov ss,ax
mov sp, offset stacktop

mov dx, 143h
mov al, 02h
out dx, al

mov dx, 141h
mov al, 0ffh
out dx, al

mov dx, 143h
mov al, 03h
out dx, al

Abc:
mov dx,141h
mov al, 0
out dx, al
call delay
mov al, 0ffh
out dx, al
call delay
jmp abc

delay:
mov cx, 0fh
outerloop:
mov bx, 0ffffh
innerloop:
nop
dec bx
jnz innerloop
dec cx
jnz outerloop
RET

code ends
end begin

Exercise 4:

Experiment:	The objective of this exercise is to create the running light effect. This effect is done by	turning on and off the lights sequentially through an array. This will create the effect that	a single light is moving across the array of LEDs.

Results:	Once again adding to the previous experiment we are able to add a running light effect:

Assume cs:code, ds:data, ss:stack

data segment
; All variables defined within the data segment
message db "Lab 5 Exercise 1$"
var db "w"
data ends

stack segment
;Stack size and the top of the stack defined in the stack segment
dw 100 dup(?)
stacktop:
stack ends

code segment
begin:

mov ax, data
mov ds,ax
mov ax, stack
mov ss,ax
mov sp, offset stacktop

mov dx, 143h
mov al, 02h
out dx, al

mov dx, 141h
mov al, 0ffh
out dx, al

mov dx, 143h
mov al, 03h
out dx, al

mov al, 01111111b
mov dx, 141h
Abc:
ror al, 1
out dx, al
call delay
jmp abc

delay:
mov cx, 0fh
outerloop:
mov bx, 0ffffh
innerloop:
nop
dec bx
jnz innerloop
dec cx
jnz outerloop
RET
code ends
end begin

Conclusion:

In conclusion we were able to complete the goal of this laboratory. We learned how to program outputs and operate LEDs based on the output. We also learned how to use NOP to create a time delay allowing us to delay the on and off functions of the LED. This was a really great lab that helped us understand the basics of I/O and assembly programming.